## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 24

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Appendix C: Macros

## Slide 4: Macro
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Write the task once and invoke it whenever it is needed
MACRO definition
    MACRO [$label] macroName parameter1, parameter2, ..., parameterN ... ... ... ... MEND
MACRO ADD3VAL $DEST, $ARG1, $ARG2, $ARG3 ADD $DEST, $ARG1, $ARG2 ADD $DEST, $DEST, $ARG3 MEND
To distinguish parameters, they must start with $
AREA CODE1, READONLY, CODE MOV R1, #5 MOV R2, #2 ADD3VAL R0, R1, R2, #5

## Slide 5: Macro
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Default Values for parameters
    MACRO ADD3VAL $DEST, $ARG1=R3, $ARG2, $ARG3=#5 ADD $DEST, $ARG1, $ARG2 ADD $DEST, $DEST, $ARG3 MEND
To use the default value, put a ‘|’ instead of the parameter
    ADD3VAL R0, R1, R2, |

## Slide 6: Using Labels in Macros
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Labels must be unique
    MACRO
  $lbl OUR_MACRO
    CMP R1,#5
    BEQ $lbl
    MOV R1, #1
  $lbl
    MEND
    AREA OURCODE, READONLY, CODE ENTRY
    MOV R1, #3
Label1 OUR_MACRO
    MOV R1, #5
Label2 OUR_MACRO
    HERE B HERE

## Slide 7: Using Labels in Macros
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Multiple labels inside a macro
    MACRO
  $lbl OUR_MACRO
    CMP R1, #5
    BEQ $lbl.equal
    MOV R1, #1
    B $lbl.next
  $lbl.equal
    MOV R1, #2
  $lbl.next
    MEND
    AREA OURCODE, READONLY, CODE
    MOV R1, #3
label1 OUR_MACRO
    MOV R1, #5
Label2 OUR_MACRO
    HERE B HERE
MOV R1, #3 CMP R1, #5 BEQ label1equal MOV R1, #1 B label1next label1equal MOV R1, #2 label1next MOV R1, #5 CMP R1, #5 BEQ label2equal MOV R1, #1 B label2next label2equal MOV R1, #2 label2next HERE B HERE

## Slide 8: Conditional Macros
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
We can pass condition into macros
  MACRO
$lbl OurMacro$cond
  CMP R1, #5
  B$cond $lbl.equal
  MOV R1, #1
$lbl.equal
  MEND
  AREA OURCODE, READONLY, CODE
  MOV R1, #3
label1 OurMacroEQ ; in the macro check equality
  MOV R1, #3
label2 OurMacroLO ; in the macro check if is lower
  HERE B HERE
MOV R1, #3
label1 OurMacroEQ
CMP R1, #5
BEQ label1equal
MOV R1, #1
label1equal
MOV R1, #3
label2 OurMacroLO
CMP R1, #5
BLO label2equal
MOV R1, #1 label2equal HERE B HERE

## Slide 9: MACRO from Files
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Include Directive

## Slide 10
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
End of Appendix C!