## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 4

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Design of Microprocessor-Based Systems (aka Embedded Systems Design and Implementation), Prabal Dutta, University of Michigan
Cortex™-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Interrupts

## Slide 4: Interrupts
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Merriam-Webster
  “to break the uniformity or continuity of”
Informs a program of some external events
Breaks execution flow
Key questions
  Where do interrupts come from?
  How do we save state for later continuation?
  How can we ignore interrupts?
  How can we prioritize interrupts?
  How can we share interrupts?

## Slide 5: I/O Data Transfer
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Two key questions to determine how data is transferred to/from a non-trivial I/O device
  How does the CPU know when data is available?
    Polling
    Interrupts
  How is data transferred into and out of the device?
    Programmed I/O
    Direct Memory Access (DMA)

## Slide 6: Interrupts
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Interrupt (a.k.a. exception or trap):
  An event that causes the CPU to stop executing the current program and begin executing a special piece of code called an interrupt handler or interrupt service routine (ISR). Typically, the ISR does some work and then resumes the interrupted program.
Interrupts are really glorified procedure calls, except that they:
  can occur between any two instructions
  are transparent to the running program (usually)
  are not explicitly requested by the program (typically)
  call a procedure at an address determined by the type of interrupt, not the program

## Slide 7: Two basic types of interrupts
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Those caused by an instruction (Trap, exception)
  TLB miss
  Illegal/unimplemented instruction
  div by 0
Those caused by the external world (interrupt, external interrupt)
  External device
  Reset button
  Timer expires
  Power failure
  System error

## Slide 8: Interrupts: How it works
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Something tells the processor core there is an interrupt
Core transfers control to code that needs to be executed
Said code “returns” to old program
Much harder than it looks
  Why?

## Slide 9: Interrupts: How it works
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
How do you figure out where to branch to?
How to you ensure that you can get back to where you started?
Don’t we have a pipeline? What about partially executed instructions?
What if we get an interrupt while we are processing our interrupt?
What if we are in a critical section?

## Slide 10: Interrupts: Where
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
If you know what caused the interrupt then you want to jump to the code that handles that interrupt
  If you number the possible interrupt cases, and an interrupt comes in, you can just branch to a location, using that number as an offset (this is a branch table)
  If you don’t have the number, you need to poll all possible sources of the interrupt to see who caused it
    Then you branch to the right code

## Slide 11: Interrupts: Snazzy architectures
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
A modern processor has many (often 50+) instructions in-flight at once
  What do we do with them?
Drain the pipeline?
  What if one of them causes an exception?
Punt all that work
  Slows us down
What if the instruction that caused the exception was executed before some other instruction?
  What if that other instruction caused an interrupt?

## Slide 12: Nested interrupts
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
If we get one interrupt while handling another what to do?
  Just handle it
    What if I’m doing something that can’t be stopped?
  Ignore it
    But what if it is important?
  Prioritize
    Take those interrupts you care about and ignore the rest

## Slide 13: Interrupt or Exception Processing Sequence
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Other code (background) is running
Interrupt trigger occurs
Processor does some hard-wired processing
Processor executes ISR (foreground), including return-from-interrupt instruction at end
Processor resumes other code
Main Code (Background)
ISR (Foreground)
Hardwired CPU response activities

## Slide 14: Interrupt or Exception Processing Sequence
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Finish current instruction (except for lengthy instructions)
Push context (8 32-bit words) onto current stack (MSP or PSP)
  xPSR, PC, LR (R14), R12, R3, R2, R1, R0
Switch to handler/privileged mode, use MSP
Load PC with address of exception handler
Load LR with EXC_RETURN code
Load IPSR with exception number
Start executing code of exception handler
Usually 16 cycles from exception request to execution of first instruction in handler

## Slide 15: 1. Finish Current Instruction
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Most instructions are short and finish quickly
Some instructions may take many cycles to execute
  Load Multiple (LDM), Store Multiple (STM), Push, Pop, MULS (32 cycles for some CPU core implementations)
This will delay interrupt response significantly
If one of these is executing when the interrupt is requested, the processor:
  abandons the instruction
  responds to the interrupt
  executes the ISR
  returns from interrupt
  restarts the abandoned instruction

## Slide 16: 2. Push Context onto Current Stack
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Two SPs: Main (MSP), process (PSP)
Which is active depends on operating mode, CONTROL register bit 1
Stack grows toward smaller addresses

## Slide 17: 3. Switch to Handler/Privileged Mode
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Handler mode always uses Main SP
Thread
Mode. MSP or PSP.
Handler Mode
MSP
Reset
Starting Exception Processing
Exception Processing
Completed

## Slide 18: Exiting an Exception Handler
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Execute instruction triggering exception return processing
Select return stack, restore context from that stack
Resume execution of code at restored address

## Slide 19: Nested Vectored Interrupt Controller (NVIC)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
NVIC manages and prioritizes external interrupts
Exception states: Inactive, Pending, Active, A&P
Processor state is automatically stored to the stack on an exception
  and automatically restored from the stack at the end of ISR
The processor supports tail-chaining
  enables back-to-back interrupts without the overhead of state saving and restoration
Late-arriving mechanism: to speed up pre-emption
Dynamic reprioritization of interrupts
Configurable number of interrupts: from 1 to 240
Configurable number of interrupt priorities: from 3 to 8 bits (8 to 256 levels)
Priority masking to support critical regions
Level and pulse detection of interrupt signals

## Slide 20: Nested Vectored Interrupt Controller
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Exception types
[Cortex-M3 Technical Reference Manual: Table 5-1]

## Slide 21: Nested Vectored Interrupt Controller
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Exception types

## Slide 22: Nested Vectored Interrupt Controller
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
NVIC register summary
Cortex-M3 Devices Generic User Guide

## Slide 23
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The End (for now)!