## Slide 1: Computer Architecture Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Instruction Set Architecture (ISA)
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Instruction Set Architecture
  A set of instructions used by a machine to run programs
  Interface between hardware & software
  Computer language vocabulary
  Provides an abstraction of hardware implementation
    Hardware implementation decides what and how instructions are implemented (microarchitecture)
  ISA specifies
    Instructions, Registers, Memory access, Input/output

## Slide 3: Key ISA Decisions
Computer Architecture-Spring 2020, AUT, Tehran, Iran
  Instruction length?
  How many registers?
  Where operands reside?
    Which instructions can access memory?
  Instruction format?
  Operand format?
    How many? How big?

## Slide 4: Where Operands Reside?
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Stack Machine
Accumulator Machine
Register-Memory Machine
Load-Store Machine
  aka Register-Register Machine

## Slide 5: Where Operands Reside?
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Stack Machine
  “0-operand” ISA
    ALU operations (add, sub, and) don’t need any operands
  “Push”
    Loads mem into 1st reg (“top of stack”),
  “Pop”
    Does reverse
  “Add”, “Sub”, “Mul”, and etc.
    Combines contents of first two regs

## Slide 6: Where Operands Reside?
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Accumulator Machine
  “1-operand” ISA
  Only 1 register
    Called “accumulator”
    Stores intermediate arithmetic & logic results
  Instructions include
    “Store”
    “Load”
    “acc  acc + mem”

## Slide 7: Where Operands Reside?
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Register-Memory Machine
  Operands
    Register or memory
  Arithmetic instructions can use data in registers and/or memory

## Slide 8: Where Operands Reside?
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Register-Registor Machine (load-store machine)
  Operands
    Register
  Arithmetic instructions can use data in registers
  No operation on memory
    Only read and write instruction (load and store)

## Slide 9: Where Operands Reside?
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Code sequence for C = A + B
Stack
Accumulator
Register-Memory
Load-Store
Push A
Load A
Load R1,A
Push B
Add B
Load R2,B
Add
Store C
Add C, A, B
Add R3,R1,R2
Pop C
Store C,R3

## Slide 10: Addressing Mode
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Where the operands are located?
Is specified by the instruction: Opcode
Addressing Modes:
  Implied mode
      Complement ACC
  Immediate Mode
      Operand is inside the instruction
      ADD R1, 105
  Register Mode
      Operand is a register
      Add R1, R2, R3
  Register Indirect Mode
          Add R1, R2, [R3]
  Auto-increment/decrement Mode: Add R1, R2, [R3+4]

## Slide 11: Addressing Mode
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Addressing Modes:
  Direct Mode
  Indirect Mode
  Relative Mode
      Relative to PC
  Index Addressing Mode
    The content of an index reg. is added to address part of the instr: Add R1, R2, [R3+Const.]
  Base Register Mode
    The address part of the intr. Is added to the content of a base reg.
    LW R1, 100(R3)

## Slide 12: RISC vs. CISC
Computer Architecture-Spring 2020, AUT, Tehran, Iran
RISC: Reduced Instruction Set Computer
CISC: Complex Instruction Set Computer
  Number of instructions
  Addressing mode
  Instruction length
  Direct memory access
  Hardware complexity
  Number of registers
  Cycles for instr. execution
  Clock frequency
  Code size