## Slide 1: Computer Architecture Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Input-Output Organization
Computer Architecture-Spring 2020, AUT, Tehran, Iran
ASCII alphanumeric Characters

## Slide 3: Input-Output Organization
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Connection to I/O
  Data bus
  Address bus
  Control signals
    Control command
    Status command
    Data output command
    Data input command

## Slide 4: Input-Output Organization
Computer Architecture-Spring 2020, AUT, Tehran, Iran
CPU connection: Memory vs I/O
  Two separate buses
  One common bus and separate control lines
  On common bus and One common control lines
Isolated I/O vs memory-mapped I/O

## Slide 5: Input-Output Organization
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Asynchronous Data Transfer
  Strobe control
    Source-initiated
    Destination-initiated

## Slide 6: Input-Output Organization
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Asynchronous Data Transfer
  Handshaking
    Source-initiated

## Slide 7: Input-Output Organization
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Asynchronous Data Transfer
  Handshaking
    Destination-initiated

## Slide 8: Direct Memory Access (DMA)
Computer Architecture-Spring 2020, AUT, Tehran, Iran
A method that allows an input/output (I/O) device to send or receive data directly to or from the main memory
  Bypassing the CPU to speed up memory operations
  Is managed by a chip known as a DMA controller (DMAC)

## Slide 9: Direct Memory Access (DMA)
Computer Architecture-Spring 2020, AUT, Tehran, Iran
DMA controller transfers the data in three modes
  Burst Mode: Here, once the DMA controller gains the charge of the system bus, then it releases the system bus only after completion of data transfer. Till then the CPU has to wait for the system buses.
  Cycle Stealing Mode: In this mode, the DMA controller forces the CPU to stop its operation and relinquish the control over the bus for a short term to DMA controller. After the transfer of every byte, the DMA controller releases the bus and then again requests for the system bus. In this way, the DMA controller steals the clock cycle for transferring every byte.
  Transparent Mode: Here, the DMA controller takes the charge of system bus only if the processor does not require the system bus.