## Slide 1: Microprocessors and Assembly language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Grading
Final Exam: 40%
Midterm Exam: 30%
Homework: 20%
Attendance: 15%
AND
Lab
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3: Course Outline
Microprocessors and microcontrollers
    How they work
    AND
    How to work with them
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 4: References
Main
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
ARMv7-M Architecture Reference Manual
Complementary material
ARM Assembly Language: Fundamentals and Techniques, 2nd Ed., William Hohl, Christopher Hinds, CRC Press, 2014.
Modern Assembly Language Programming with the ARM Processor, Larry D. Pyeatt, Elsevier, 2016.
Embedded Systems:Introduction to ARM®CORTEX-M Microcontrollers, Vol. 1, 5th Ed., Jonathan W. Valvano, 2014.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 5: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Computer Organization & Design, The Hardware/Software Interface, 3rd Edition, by D. Patterson and J. Hennessey, Morgan Kaufmann publishing, 2005.
“Computer Organization & Design” handouts, by Prof. Kumar, UIUC, Fall 2007.
“Computer Organization I” handouts, FSU, Fall 2007.
“Machine Structures” handouts, by Prof. D. Garcia, UCB, Spring 2010.
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
“Computer Organization & Language” handouts, Dept. of CE, SUT, by Prof. H. Asadi, 2016.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 6: Computer History
Mechanical Computers
Electro-Mechanical Computers
Electronic Computers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 7: Computer History
Mechanical Computers
  Abacus
  Mechanical calculators
    Pascal’s calculator (1642)
    Curta (1930s)
  Punched-card data processing (1725, 1800s, 1900s)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 8: Computer History
Mechanical Computers
  Difference engine: Charles Babbage (1791-1871)
    First general-purpose computing device
  Analytical engine
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 9: Computer History
Electro-Mechanical Computers
  Switches, relays
  Early 1900s
  Zuse’s Z2, Z3, Z4 (world's first commercial digital computer, mechanical memory)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 10: Computer History
Electronic Computers
  1st generation
    vacuum tubes (1945-1955)
    ENIAC, 1946
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 11: Computer History
Electronic Computers
  2nd generation
    BJT transistors (1955-1965)
    CDC 6600 (1964-1969)
      world's fastest computer from 1964 to 1969
      $2,370,000
      30kW, 6tons
      10MHz, 2 MIPS
      Up to 982 kilobytes
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 12: Computer History
Electronic Computers
  3rd generation
    integrated circuits (1965-1974)
    Intel 4004 (1971)
      The first commercially available microprocessor
      10 µm process
      92,000 instructions per second
      1 MHz clock rate
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 13: Computer History
Electronic Computers
  4th generation: VLSI
    1974-1989
  5th generation: ULSI
    1990-present
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 14: Computer History
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Year | Technology Used in Computers | Relative Performance per unit cost
~1950 | Vacuum tube | 1
1960s | Transistor | 35
1975 | Integrated circuit | 900
1995 | Very large scale integrated circuit | 2,400,000
2005 | Ultra large scale integrated circuit | 6,200,000,000

## Slide 15: Computer History
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
What happened from 1970?
  Transistor count doubles every 24-month

## Slide 16
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Instruction Set Architecture
(ISA)

## Slide 17: Instruction Set Architecture (ISA)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
A set of instructions used by a machine to run programs
Interface between hardware & software
Computer language vocabulary
Provides an abstraction of hardware implementation
  Hardware implementation decides what and how instructions are implemented
ISA specifies
  Instructions, Registers, Memory access, Input/output
Applications
Compilers
Operating System
Architecture (ISA)
Microarchitecture
Digital Design
Circuit
Device

## Slide 18: Instruction Set Architecture (ISA)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
How many instructions needed?
What functionalities required?
  Load/store
  Control
  Arithmetic/logic

## Slide 19: Instruction Set Architecture (ISA)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Key ISA decisions
  Instruction length
  Number, length, and types of registers
  Where operands reside
  How to access memory
  Instruction format
  Operand format
    How many and how big

## Slide 20: Instruction Set Architecture (ISA)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Instruction length
Variable:
x86 – Instructions vary from 1 to 17 Bytes long
VAX – from 1 to 54 Bytes
MIPS, PowerPC, ARM:
all instruction are 4 Bytes long
Fixed:

## Slide 21: ISA: Instruction length
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Variable-length instructions
  Require multi-step fetch and decode
  Allow for a more flexible and compact instruction set
  CISC processors like x86 & VAX
    Complex Instruction Set Computing
Fixed-length instructions
  Allow easy fetch and decode
  Simplify pipelining and parallelism
  RISC processors like MIPS & PowerPC
    Reduced Instruction Set Computing

## Slide 22: ISA: RISC vs. CISC
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Early Trend
  Adding more instructions to next generation CPUs to do more complicated operations
  VAX arch had an instruction to multiply polynomials!
CISC Philosophy
  Limited main memory + immature compilers
    More dense instructions, highly encoded, variable length instructions
  Data loading as well as calculation

## Slide 23: ISA: RISC vs. CISC
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
RISC Philosophy
  Keep ISA small and simple
    Makes it easier to build faster hardware
  Let SW do complicated operations by composing simpler instructions
Note on “Reduced" in RISC Phrase
  Amount of work any single instruction accomplishes reduced
    Single ALU operation, single memory access, …

## Slide 24: ISA: RISC vs. CISC
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
CISC Problems
  Performance tuning challenging
    Complex/high-level instructions rarely used
  Slower clock rates
  Longer time-to-market
    Due to prolonged design time
CISC Features
  Ease compiler implementation
    HW supports all kind of addressing modes

## Slide 25: ISA: RISC vs. CISC
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
RISC Features
  Low complexity
    Less error-prone HW implementation
  Implementation advantages
    Less transistors
    Extra space: more registers, cache
  Marketing
    Reduced design time

## Slide 26: ISA: RISC vs. CISC
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
RISC vs. CISC
Hangul vs. Hiragana

## Slide 27: ISA: How Many Registers?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Advantages of a small number of registers
  Requires fewer bits to specify which one
  Less hardware
  Faster access
    Shorter wires
    Faster index decoding (fewer logic levels)
  Faster context switch (your OS course!)
    When all registers need saving

## Slide 28: ISA: How Many Registers?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Advantages of a larger number of registers
  Fewer loads and stores needed
    Less data transfer between CPU & memory
  Easier to do several operations at once

## Slide 29: ISA: Where Operands Reside?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Stack Machine
Accumulator Machine
Register-Memory Machine
Load-Store Machine
  aka Register-Register Machine

## Slide 30: ISA: Where Operands Reside?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Code sequence for C = A + B
Stack
Accumulator
Register-Memory
Load-Store
Push A
Load A
Load R1,A
Push B
Add B
Load R2,B
Add
Store C
Add C, A, B
Add R3,R1,R2
Pop C
Store C,R3

## Slide 31: Harvard vs. Von Neumann Arch.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 32
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Types of Computer Systems

## Slide 33: Types of Computer Systems
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Desktops
  General purpose
  Market dominated by x86 processors
  Various software
  For use by individuals
Servers and Warehouse-Scale Computers (WSCs)
  Thousands of cores and disks
  Market dominated by x86-compatible server chips
  Dedicated apps, plus cloud hosting of virtual machines
  Increasing use of GPUs, FPGAs, and custom hardware to accelerate workloads

## Slide 34: Types of Computer Systems
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Mobile (smartphone/tablet)
    >1 billion sold/year
    Market dominated by ARM-ISA-compatible general-purpose processor in system-on-a-chip (SoC)
    Plus sea of custom accelerators (radio, image, video, graphics, audio, motion, location, security, etc.)
  Anything Else?

## Slide 35: Types of Computer Systems
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Embedded systems

## Slide 36: Design Criteria
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Performance
Power consumption
Energy consumption
Area
Weight
Design cost
Implementation cost
Time to market
Maintainability
Debugging
Flexibility
Scalability
…

## Slide 37: Options for Building Embedded Systems
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Dedicated hardware
  ASIC (Application-specific integrated circuit)
  Programmable logic (FPGA, PLD)
Software running on generic hardware
  Microprocessor + memory + peripherals
  Microcontroller (internal memory & peripherals)
A combination of all options (Complex systems)

## Slide 38: Microprocessor vs. Microcontroller
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Microprocessor
  An IC that has only CPUs inside it
  No RAM, ROM, or other peripheral
Microcontroller (MCU)

## Slide 39: Microprocessor vs. Microcontroller
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Microprocessor
Microcontroller (MCU)

## Slide 40: Microprocessor vs. Microcontroller
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Microprocessor | Microcontroller
Heart of computer systems | Heart of embedded systems
It is just a processor. Memory and I/O components are connected externally | Has processor along with internal memory and I/O components
Since memory and I/O have to be connected externally, the circuit becomes larger | Since memory and I/O have to be connected externally, the circuit is small
Cannot be used in compact system | It is efficient for compact systems
The entire energy consumption is high due to external components | Suitable for battery-operated systems
Slow memory access | Fast memory access
Is based on Von Neumann architecture (program and data are stored in the same memory module) | Is based on Harvard architecture (program and data memory are separate)