## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 12

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
https://www.analogictips.com/pulse-width-modulation-pwm/
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Pulse Width Modulation (PWM)

## Slide 4: PWM: What is it and how does it work?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Digital signals have two positions
  on or off, interpreted in shorthand as 1 or 0
Analog signals can be
  on, off, half-way, two-thirds the way to on, and an infinite number of positions between 0 and 1
To take an analog input signal (e.g., temperature) into a microcontroller
  by using an analog-to-digital converter
  But what about outputs?
PWM is a way to control analog devices with a digital output
  Drive analog devices like variable-speed motors, dimmable lights, actuators, and speakers
https://www.analogictips.com/pulse-width-modulation-pwm/

## Slide 5: PWM: What is it and how does it work?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
PWM is not true analog output
  PWM “fakes” an analog-like result by applying power in pulses, or short bursts of regulated voltage
  Is a fancy term for describing a type of digital signal
https://www.analogictips.com/pulse-width-modulation-pwm/

## Slide 6: PWM: What is it and how does it work?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
A device that is driven by PWM ends up behaving like the average of the pulses
The average voltage level can be a steady voltage or a moving target (dynamic/changing over time)
https://www.analogictips.com/pulse-width-modulation-pwm/
Average Voltage =
Duty Cycle x High Voltage Level

## Slide 7: PWM: An Example
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Controlling the brightness of an LED by adjusting the duty cycle
With an RGB (red green blue) LED,
  you can control how much of each of the three colors you want in the mix of color by dimming them with various amounts
https://www.analogictips.com/pulse-width-modulation-pwm/

## Slide 8: PWM in SAM3X
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The PWM macrocell controls 8 channels independently
  Each channel controls two complementary square output waveforms
Embedded Characteristics
  Common Clock Generator Providing Thirteen Different Clocks
    A Modulo n Counter Providing Eleven Clocks
    Two Independent Linear Dividers Working on Modulo n Counter Outputs
  Independent Clock Selection for Each Channel
  Independent Period, Duty-Cycle and Dead-Time for Each Channel
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 9: PWM in SAM3X
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
PWM Clock Generator
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 10
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The End!