## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 13

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
ARM Architecture and Assembly Language Programming

## Slide 4: ARM Registers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 5: Registers Data Size
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
MSB: D31
LSB: D0

## Slide 6: General Purpose Registers
13 GPRs
  R0-R12 (32-bit)
  Can be used by all arithmetic/logic instructions
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 7: ARM Instruction Format
A common format
Instruction destination, source1, source2
Source2 can be
  A register
  Immediate (constant)
  Memory
Destination is often
  A register
  Memory
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 8: MOV Instruction
Copies data into register or from register to register
MOV Rn, Op2
load Rn register with Op2 (Operand2)
  Op2 can be immediate (an 8-bit value)
  Op2 can be a register Rm
Rn or Rm can be any of the registers R0 to R15
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 9: MOV Instruction: Examples
Load R2 with 0x25 (R2 = 0x25)
MOV R2,#0x25; 25 in hex
  Notice the # before immediate values
  Use “;” for comment (same as “//” in C)
  For numbers in hex, put “0x” in front of the value
    Put nothing for decimal
    MOV R1,#50; 50 in decimal
Copy contents of R7 into R5 (R5 = R7)
MOV R5,R7
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 10: MOV Instruction: Examples
On moving a constant,
  What happens to the rest of the register’s bits?
  What about moving an immediate larger than 255?
MOV R1,#505
    Will cause an error! Why?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 11: ADD Instruction
ADD Rd,Rn,Op2
Add Rn to Op2 and store the result in Rd
  Op2 can be immediate (an 8-bit value)
  Op2 can be a register Rm
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 12: A Simple Program
Add 0x25 and 0x34
MOV R1,#0x25
MOV R7,#0x34
ADD R5,R1,R7
OR
MOV R1,#0x25
ADD R5,R1,#0x34
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 13
WHY
To Learn Assembly?!!!
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran