## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 14

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3: Why to Learn Assembly Language
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
HLL can greatly enhance programmer productivity, BUT
Writing assembly code is desirable or necessary for
  The first steps in booting the computer
  Code to handle interrupts
  Low-level locking code for multi-threaded programs
  Code for machines where no compiler exists
  Code which needs to be optimized beyond the limits of the compiler
  On computers with very limited memory
  Code that requires low-level access to architectural and/or processor features
  Write a compiler
  Program device drivers

## Slide 4
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
ARM Architecture and Assembly Language Programming

## Slide 5: SUB Instruction
We have already seen MOV and ADD instr.
SUB Rd, Rn, Op2 ; Rd = Rn – Op2
A simple code
MOV R1, #0x34 ; load 0x34 into R1 (R1 = 0x34) SUB R5, R1, #0x25 ; R5 = R1 – 0x25 (R5 = 0x34 – 0x25)
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 6: ALU Instructions Using GPRs
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 7: The ARM Memory Map
Memory space allocation in the ARM
  4 gigabytes of directly accessible memory space
    from 0 to 0xFFFFFFFF
Memory space can be divided into five sections
  On-chip peripheral and I/O registers
  On-chip data SRAM
  On-chip EEPROM (for saving critical data)
  On-chip Flash ROM (program space)
  Off-chip DRAM space
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 8: The ARM Memory Map
Why both EEPROM and Flash?
Why both SRAM and EEPROM?
IO-mapped or Memory-Mapped IO?
Memory space is 4GB; is it enough?
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 9: The ARM Memory Map
Q: A given ARM chip has the following address assignments. Calculate the space and the amount of memory given to each section.
(a) Address range of 0x00100000 – 0x00100FFF for EEPROM
  (b) Address range of 0x40000000 – 0x40007FFF for SRAM
  (c) Address range of 0x00000000 – 0x0007FFFF for Flash
  (d) Address range of 0xFFFC0000 – 0xFFFFFFFF for peripherals
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
peripherals