## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 16

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
ARM Data Format, Pseudo-instructions and Directives

## Slide 4: ARM Data Format
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Data format representation
  Hexadecimal numbers
  MOV R1, #0x99
  Decimal numbers
  MOV R7, #12
  Binary numbers
  MOV R6, #2_10011001
  Numbers in any base between 2 and 9
  MOV R7, #8_33
  ASCII characters
  LDR R3, #'2' ; R3 = 00110010 or 32 in hex

## Slide 5: Pseudo-instructions
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
LDR pseudo-instruction
  Limitation of loading immediate value: 8-bit
    MOV Rd, 0x11223344
    LDR Rd, =32-bit_immediate_value
    LDR R7, =0x11223344
Load registers with the addresses of memory locations
    ADR Rn, label

## Slide 6: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives give directions to the assembler
  Some Widely Used ARM Directive

## Slide 7: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: AREA
  Defines a new section of memory
  AREA sectionname, attribute, attribute, ...
  Some attributes: CODE, DATA, READONLY, READWRITE, and ALIGN
  AREA MY_ASM_PROG1, CODE, READONLY

## Slide 8: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: AREA
  Attributes: READONLY
    All the READONLY sections of the same program are put next to each other in the flash memory by the linker
  Attributes: READWRITE
    The linker puts all the READWRITE sections of the same program next to each other in the SRAM memory
  Attributes: CODE: is by default READONLY memory
  Attributes: DATA: is by default READWRITE memory
  Attributes: ALIGN: to align a section

## Slide 9: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: END
  Indicates to the assembler the end of the source code
  Is the last line of the ARM assembly program
    Anything after the END directive in the source file is ignored by the assembler
        AREA PROG_2_1, CODE, READONLY MOV R1, #0x25 ; R1 = 0x25 MOV R2, #0x34 ; R2 = 0x34 ADD R3, R2, R1 ; R3 = R2 + R1
    HERE B HERE ; stay here forever
      END