## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 17

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
ARM Data Format, Pseudo-instructions and Directives (cont.)

## Slide 4: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: EQU (equate)
  To define a constant value or a fixed address by a name
    To make the program easier to read
        COUNT EQU 0x25
        MOV R2, #COUNT ; R2 = 0x25
        MOV R2, #0x25
    Avoid searching the entire program trying to find and change every occurrence of a variable
Converted by Assembler to

## Slide 5: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: EQU (equate)
  Using EQU for fixed data assignment
        DATA1 EQU 0x39 ; the way to define hex value
        DATA2 EQU 2_00110101 ; the way to define binary value (35 in hex)
        DATA3 EQU 39 ; decimal numbers (27 in hex)
        DATA4 EQU '2' ; ASCII characters
  Using EQU for special register address assignment
        FIO2SET0 EQU 0x3FFFC058 ; PORT2 output set register 0 address
        MOV R6, #0x01 ; R6 = 0x01
        LDR R2, =FIO2SET0 ; R2 = 0x3FFFC058
        STRB R6, [R2] ; Write 0x01 to FIO2SET0

## Slide 6: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: EQU (equate)
  Using EQU for RAM address assignment
        SUM EQU 0x40000120 ; assign RAM location to SUM
        MOV R2, #5 ; load R2 with 5
        MOV R1, #2 ; load R1 with 2
        ADD R2, R2, R1 ; R2 = R2 + R1
        LDR R3, =SUM ; load R3 with 0x40000120
        STRB R2, [R3] ; store the result SUM
Directives: RN (equate)
  To give a CPU register a name
        VAL1 RN R1 ; define VAL1 as a name for R1
        VAL2 RN R2 ; define VAL2 as a name for R2
        SUM RN R3 ; define SUM as a name for R3

## Slide 7: Assembler Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: INCLUDE
  Tells the ARM assembler to read in the content of a file to the current program file

## Slide 8: Assembler Data Allocation Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives to allocate memory and initialize its value
Directives: DCB
  define constant byte
        MYVALUE DCB 5 ; MYVALUE = 5
        MYMSAGE DCB "HELLO WORLD" ; ASCII string
Each alphanumeric letter in a string is converted to its ASCII encoding value
Directives: DCW => define constant half-word
        MYDATA DCW 0x20, 0xF230, 5000, 0x9CD7
Directives: DCD => define constant word
        MYDATA DCD 0x200000, 0x30F5, 5000000, 0xFFFF9CD7

## Slide 9: Assembler Data Allocation Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
An sample program
    AREA LOOKUP_EXAMPLE, READONLY, CODE
    LDR R2, =OUR_FIXED_DATA ; point to OUR_FIXED_DATA
    LDRB R0, [R2] ; load R0 with the contents of memory pointed to by R2
    ADD R1, R1, R0 ; add R0 to R1
  HERE B HERE ; stay here forever
    OUR_FIXED_DATA
    DCB 0x55, 0x33, 1, 2, 3, 4, 5, 6
    DCD 0x23222120, 0x30
    DCW 0x4540, 0x50
    END
ADR R2, OUR_FIXED_DATA

## Slide 10: Assembler Data Allocation Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives to allocate memory and initialize its value
Directives: SPACE
  To allocate memory for variables without initial values
        LONG_VAR SPACE 4 ; Allocate 4 bytes
        OUR_ALFA SPACE 2 ; Allocate 2 bytes
Directives: ALIGN
  To make sure data is aligned on the 32-bit word or 16-bit half word address boundary
      ALIGN 4 ; the next instruction is word (4 bytes) aligned
      ...
      ALIGN 2 ; the next instruction is half-word (2 bytes) aligned
      ...

## Slide 11: Assembler Data Allocation Directives
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Directives: ALIGN
AREA E2_7A, READONLY, CODE ADR R2, DTA LDRB R0, [R2] ADD R1, R1, R0 H1 B H1 DTA DCB 0x55 DCB 0x22 END
DTA DCB 0x55 ALIGN 2 DCB 0x22 END
DTA DCB 0x55 ALIGN 4 DCB 0x22 END

## Slide 12: Rules for Labels in Assembly Language
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Each label name must be unique in the file
label names consist of
  Alphabetic letters in both uppercase and lowercase
  The digits 0 through 9, and
  The special characters underscore ‘_’
The first character of the label must be
  An alphabetical letter or underscore
    Cannot be a numeral
    Cannot be reserved words (ADD, MOV, …)

## Slide 13
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Creating an ARM Assembly Program

## Slide 14: Creating an ARM Assembly Program
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Steps to create a program

## Slide 15: Creating an ARM Assembly Program
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Sample of a Map File

## Slide 16: Creating an ARM Assembly Program
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Sample of a List File

## Slide 17: Power up Location for ARM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Q: At what address does the CPU wake up to when power is applied or when the CPU is reset?
  ARM7 microcontrollers: 0x00000000
    The first instruction is expected to be stored here
BUT, ARM Cortex-M is different
  Reads from 0x00000004-0x00000007 and
  Put them into the program counter, then
  CPU fetches the first instruction using the content of PC
  The programmer (working with the software tools) shall put the starting address of the program at memory location 0x00000004