## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 18

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Instruction Formation of the ARM

## Slide 4: Instruction Formation
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
General formation of data processing instructions
  Cond [31:28]: Condition field (will be discussed in Ch. 4)
  [27:26]: Always “00”
  I [25]: Defines the type of second operand
    I = 1: Op2 is an immediate value
  [24:21]: Opcode
  S [20]: Update CPSR

## Slide 5: Instruction Formation
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
ADD instruction format
SUB instruction format
Branch (B) instruction format

## Slide 6: Little Endian vs. Big Endian War
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Little endian
  Low byte goes to the low memory location
  High byte goes to the high memory address
  All Intel processors
Big endian
  Low byte goes to the high memory location
  High byte goes to the low memory address
  Freescale (formerly Motorola and now NXP)
ARM allows the software designer to choose!
  A hardware switch that is controlled by software

## Slide 7
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Some ARM Addressing Modes

## Slide 8: Addressing Modes
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Addressing Mode
  The various ways operands are specified in the instruction
  Is the way CPU generates address from instruction to read/write the operands
Three basic modes
  Register
  Immediate
  Register indirect (indexed addressing mode)

## Slide 9: Addressing Modes
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Register Addressing Mode
Immediate addressing mode
Register Indirect addressing mode (Indexed)

## Slide 10: Addressing Modes
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Register Indirect addressing mode (Indexed)
  Can be used for pointer implementation
char *ourPointer; ourPointer = (char*) 0x12456; //Point to location 12456 *ourPointer = 25; //store 25 in location 0x12456 ourPointer ++; //point to next location
LDR R2, =0x12456 ; point to location 0x12456 MOV R0, #25 ; R0 = 25 STRB R0, [R2] ; store R0 in location 0x12456 ADD R2, R2, #1 ; increment R2 to point to next location

## Slide 11
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
End of Chapter 2!