## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 20

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Branch, Call, and Looping in ARM

## Slide 4: Looping in ARM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Using instruction BNE for looping
    BACK ......... ; start of the loop ......... ; body of the loop ......... ; body of the loop SUBS Rn, Rn, #1 ; Rn = Rn - 1, set the flag Z = 1 if Rn = 0 BNE BACK ; branch if Z = 0
    ; --- this program adds value 9 to the R0 a 1000 times ---
    AREA EXAMPLE4_1, CODE, READONLY
    LDR R2, =1000 ; R2 = 1000 (decimal) for counter
    MOV R0, #0 ; R0 = 0 (sum)
    AGAIN ADD R0, R0, #9 ; R0 = R0 + 9 (add 09 to R1, R1 = sum)
    SUBS R2, R2, #1 ; Decrement counter and set the flags.
    BNE AGAIN ; repeat until COUNT = 0 (when Z = 1)
    MOV R4, R0 ; store the sum in R4
    HERE B HERE ; stay here
    END

## Slide 5: Looping in ARM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Loop inside a loop
    AREA EXAMPLE4_3, CODE, READONLY
        MOV R0, #0x55 ; R0 = 0x55
      MOV R2, #16 ; load 16 into R2 (outer loop count)
    L1 LDR R1, =1000000000 ; R1 = 1,000,000,000 (inner loop count)
    L2 EOR R0, R0, #0xFF ; complement R0 (R0 = R0 Ex-OR 0xFF)
        SUBS R1, R1, #1 ; R1 = R1 – 1, decrement R1 (inner loop)
        BNE L2 ; repeat it until R1 = 0
        SUBS R2, R2, #1 ; R2 = R2 – 1, decrement R2 (outer loop)
        BNE L1 ; repeat it until R2 = 0
    HERE B HERE ; stay here
    END

## Slide 6: Looping in ARM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Conditional Branch Instructions for Unsigned Data

## Slide 7: Looping in ARM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Comparison of unsigned numbers
    CMP Rn, Op2
    LDR R1, =0x35F ; R1 = 0x35F
    LDR R2, =0xCCC ; R2 = 0xCCC
    CMP R1, R2 ; compare 0x35F with 0xCCC
    BCC OVER ; branch if C = 0
    MOV R1, #0 ; if C = 1, then clear R1
OVER ADD R2, R2, #1
; R2 = R2 + 1 = 0xCCC + 1 = 0xCCD

## Slide 8: Branch Instruction
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 9: Branch Instruction
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 10: Branching beyond 32MB byte limit
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Branch and exchange
    BX Rn

## Slide 11: Calling Subroutine with BL
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
BL: Branch and Link

## Slide 12: Calling Subroutine with BL
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Delay subroutine
AREA EXAMPLE4_8, CODE, READONLY
    RAM_ADDR EQU 0x40000000 ; change the address for your ARM
    LDR R1, =RAM_ADDR ; R1 = RAM address
AGAIN MOV R0, #0x55 ; R0 = 0x55
    STRB R0, [R1] ; send it to RAM
    BL DELAY ; call delay (R14 = PC of next instruction)
    MOV R0, #0xAA ; R0 = 0xAA
    STRB R0, [R1] ; send it to RAM
    BL DELAY ; call delay
    B AGAIN ; keep doing it
    ; --------------------DELAY SUBROUTINE
DELAY LDR R3, =5 ; R3 =5, modify this value for different delay
L1 SUBS R3, R3, #1 ; R3 = R3 - 1
    BNE L1
    BX LR ; return to caller; --------------------end of DELAY subroutine
END ; notice the place for END directive

## Slide 13: Main Program and Calling Subroutines
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 14: Conditional Execution
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
A unique feature of ARM
  conditional execution for ALL instructions

## Slide 15: Conditional Execution
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Conditional MOV
    MOV R1, #10; R1 = 10 MOV R2, #12; R2 = 12 CMP R2, R1; compare 12 with 10, Z=0 because they are not equal MOVEQ R4, #20; this line is not executed because the condition EQ is not met
Conditional ADD with ‘S’ suffix
    ADDNES R1, R1, #10 ; this line is executed and set the flags if Z = 0

## Slide 16
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
End of Chapter 4!