## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 22

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
ARM Memory Map, Memory Access, and
Stack

## Slide 4: Memory Addressing
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Memory Byte Addressing in ARM

## Slide 5: Memory Addressing
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Sample Memory Space Allocation in ARM

## Slide 6: AHB and APB buses
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
AHB: advanced high-performance bus
  Connects CPU to RAM, ROM, …
APB: advanced peripherals bus
  Dedicated for communication with the on-chip peripherals
    timers, ADC, UART, SPI, I2C, …

## Slide 7: Data Misalignment in SRAM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Compilers make sure that instructions are always aligned
Placement of data in SRAM can be nonaligned
  Memory access penalty

## Slide 8: Data Misalignment in SRAM
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
    LDR R1, =0x40000000 ; R1=0x40000000
    LDR R2, =0x4598F31E ; R2=0x4598F31E
    STR R2, [R1] ; Store R2 to location 0x40000000
    ADD R1, R1, #1 ; R1 = R1 + 1 = 0x40000001
    STR R2, [R1] ; Store R2 to location 0x40000001

## Slide 9: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Base plus offset addressing modes
  Pre-indexed addressing mode with fixed offset
    LDR R5, =0x55667788
    LDR R1, =0x10000000; load the address of first location
    STR R5, [R1] ; store R5 to location 0x10000000
    STR R5, [R1, #4]; store R5 to location 0x10000000 + 4 (0x10000004)
    STR R5, [R1, #8]; store R5 to location 0x10000000 + 8 (0x10000008)
    STR R5, [R1, #0x0C]; store R5 to location 0x10000000 + 0x0C (0x1000000C)

## Slide 10: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Base plus offset addressing modes
      Pre-indexed addressing mode with writeback and fixed offset
        The calculated pointer is written back to the pointing register
        LDR R1, =0x10000000 ; load the address of first location
        STR R5, [R1] ; store R5 to location 0x10000000
        STR R5, [R1, #4]!; store R5 to location 0x10000000 + 4 (0x10000004)
        ; writeback makes R1 = 0x10000004
        STR R5, [R1, #4]!; store R5 to location 0x10000004 + 4 (0x10000008)
        ; writeback makes R1 = 0x10000008
        STR R5, [R1, #4]!; store R5 to location 0x10000008 + 4 (0x1000000C)
        ; writeback makes R1 = 0x1000000C

## Slide 11: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Base plus offset addressing modes
      Post-indexed addressing mode with fixed offset
        Update pointer after the load/store operation
        STR R1, [R2], #4 ; store R1 into memory pointed to by R2 and then write back R2 + 4 to R2
        LDRB R5, [R3], #1 ; load a byte from memory pointed to by R3 and then write back R3 + 1 to R3

## Slide 12: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Pre-indexed address mode with offset of a shifted register
      Simple format
        LDR Rd, [Rm, Rn] ; Rd is loaded from location Rm + Rn of memory
        STR Rs, [Rm, Rn] ; Rs is stored to location Rm + Rn of memory
      General format
        LDR Rd, [Rm, Rn, <shift>] ; (Shifted Rn) + Rm is used as the address
        STR Rd, [Rm, Rn, <shift>] ; (Shifted Rn) + Rm is used as the address
        LDR R1, [R2, R3, LSL #2] ; R2 + (R3 × 4) is used as the address
        STR R1, [R2, R3, LSL #1] ; R2 + (R3 × 2) is used as the address
        STRB R1, [R2, R3, LSL #2] ; R2 + (R3 × 4) is used as the address
        ; least significant byte of R1 is stored at location R2 + (R3 × 4)
        LDR R1, [R2, R3, LSR #2] ; R2 + (R3 / 4) is used as the address

## Slide 13: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Writeback sign (!) in pre-indexed ld/st with scaled register
        LDR R1, [R2, R3, LSL #2]!; R2 + (R3 × 4) is used as the address,
            ; content of location R2 + (R3 × 4) is loaded to R1
            ; R2 = R2 + (R3 × 4) (R2 is updated.)
        STR R1, [R2, R3, LSL #1]!; R2 + (R3 × 2) is used as the address
                ; R1 is stored to location R2 + (R3 × 2)
            ; R2 = R2 + (R3 × 2) (R2 is updated)
    Scaled register post-indexed
        STR R1, [R2], R3, LSL #2; store R1 at location R2 of memory ; and write back R2 + (R3 × 4) to R2. LDR R1, [R2], R3, LSL #2; load location R2 of memory to R1 ; and write back R2 + (R3 × 4) to R2

## Slide 14
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
To be Continued!