## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 6

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Design of Microprocessor-Based Systems (aka Embedded Systems Design and Implementation), Prabal Dutta, University of Michigan
Cortex™-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Parallel Input/Output Controller (PIO)

## Slide 4: PIO Description
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Parallel Input/Output Controller (PIO)
  manages up to 32 fully programmable input/output lines
  Each I/O line may be dedicated as a general-purpose I/O or be assigned to a function of an embedded peripheral
Each I/O line of the PIO Controller features
  An input change interrupt enabling level change detection on any I/O line.
  Additional Interrupt modes enabling rising edge, falling edge, low level or high level detection on any I/O line.
  A glitch filter providing rejection of glitches lower than one-half of system clock cycle
  A debouncing filter providing rejection of unwanted pulses from key or push button operations
  Multi-drive capability similar to an open drain I/O line
  Control of the pull-up of the I/O line
  Input visibility and output control
  A synchronous output providing up to 32 bits of data output in a single write operation
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 5: PIO Description
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Parallel Input/Output Controller (PIO)
  Each PIO Controller controls up to 32 programmable I/O Lines
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 6: PIO Block Diagram
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 7: Product Dependencies
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Pin Multiplexing
  Each pin is configurable, according to product definition
    A general-purpose I/O line only
    An I/O line multiplexed with one or two peripheral I/Os
Power Management
  Controls the PIO Controller clock in order to save power
  Writing any of the registers of the user interface does not require the PIO Controller clock to be enabled
  Not all of the features of the PIO Controller are available when the clock is disabled
    Input Change Interrupt, Interrupt Modes on a programmable event and the read of the pin level require the clock to be validated
  After a hardware reset, the PIO clock is disabled by default
  The user must configure the Power Management Controller before any access to the input line information
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 8: Product Dependencies
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Interrupt Generation
  The PIO Controller is connected on one of the sources of the NVIC
    Using the PIO Controller requires the NVIC to be programmed first
    The PIO Controller interrupt can be generated only if the PIO Controller clock is enabled
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 9: Functional Description
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 10: Functional Description
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Pull-up Resistor Control
  PIO_PUER: Pull-up Resistor Control
  PIO_PUSR: Pull-up Status Register
  After reset, all of the pull-ups are enabled, i.e. PIO_PUSR resets at the value 0x0
I/O Line or Peripheral Function Selection
  PIO_PER: PIO Enable Register
  PIO_PDR: PIO Disable Register
  PIO_PSR: PIO Status Register
    indicates whether the pin is controlled by the corresponding peripheral or by the PIO Controller, if 0:
    pin is controlled by the corresponding on-chip peripheral selected in the PIO_ABSR (AB Select Register)

## Slide 11: Functional Description
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Output Control
  PIO_OER: Output Enable Register
  PIO_ODR: Output Disable Register
  PIO_OSR: Output Status Register
    When a bit in this register is at 0, the corresponding I/O line is used as an input only
    When the bit is at 1, the corresponding I/O line is driven by the PIO controller
  PIO_SODR: Set Output Data Register
  PIO_CODR: Clear Output Data Register
  PIO_ODSR: Output Data Status Register

## Slide 12: Functional Description
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Chapter 31: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Synchronous Data Output
  Simultaneous write into PIO_SODR and PIO_CODR is not possible
  PIO Controller offers a direct control of PIO outputs by single write access to PIO_ODSR
Multi Drive Control (Open Drain)
  Permits several drivers to be connected on the I/O line which is driven low only by each device
  PIO_MDER: Multi-driver Enable Register
  PIO_MDSR: indicates the pins that are configured to support external drivers
  After reset, the Multi Drive feature is disabled on all pins (PIO_MDSR = 0)

## Slide 13
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The End!