## Slide 1: Microprocessors and Assembly Language Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 9

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
http://www.circuitbasics.com/basics-uart-communication/
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Universal Asynchronous Receiver/Transmitter (UART)

## Slide 4: Basics of UART Communication
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Asynchronous serial communication
  Uses two wires to transmit data between devices
  Data flows from the Tx pin of the transmitting UART
    to the Rx pin of the receiving UART
  No clock signal to synchronize the output of bits from the transmitting UART
    to the sampling of bits by the receiving UART
http://www.circuitbasics.com/basics-uart-communication/

## Slide 5: UART Communication Details
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The transmitting UART adds start and stop bits
  to the data packet being transferred
These bits define the beginning and end of the data packet
  so the receiving UART knows when to start reading the bits
The receiving UART detects a start bit
  Then, starts to read the incoming bits
    at a specific frequency known as the baud rate
Baud rate: a measure of the speed of data transfer
  expressed in bits per second (bps)
The baud rate between the transmitting and receiving UARTs can only differ by about 10%
http://www.circuitbasics.com/basics-uart-communication/

## Slide 6: UART Communication Details
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
When not transmitting data
  The UART transmission line is held at a high voltage level
START BIT
  The transmitting UART pulls the line from high to low for one clock cycle
STOP BITS
  The sending UART drives the data transmission line from a low voltage to a high voltage for at least two bit durations
http://www.circuitbasics.com/basics-uart-communication/

## Slide 7: UART in SAM3X8E
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Independent Receiver and Transmitter
  with a Common Programmable Baud Rate Generator
Even, Odd, Mark or Space Parity Generation
Parity, Framing and Overrun Error Detection
Interrupt Generation
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 8: UART in SAM3X8E
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The UART pins are multiplexed with PIO lines
The programmer must first configure the PMC to enable the UART clock
  PMC: Power Management Controller
Only 8-bit character is supported (with parity)
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 9: Baud Rate Generator in SAM3X8E
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The baud rate clock
  Is the master clock divided by 16 times the value (CD) written in UART_BRGR (Baud Rate Generator Register)
  If UART_BRGR is set to 0, the baud rate clock is disabled and the UART remains inactive
The maximum allowable baud rate is Master Clock divided by 16
  The minimum allowable baud rate is Master Clock divided by (16 x 65536)
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 10: Baud Rate Generator in SAM3X8E
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 11: UART Receiver in SAM3X8E
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Receiver Reset, Enable and Disable
  After device reset, the UART receiver is disabled
  To enable: RXEN = 1 in the control register (UART_CR)
  If enabled: the receiver starts looking for a start bit
  To disable: RXDIS = 1 in the control register (UART_CR)
    If the receiver is waiting for a start bit, it is immediately stopped
    If the receiver has already detected a start bit and is receiving the data, it waits for the stop bit before actually stopping its operation
  To reset: RSTRX =1 in the control register (UART_CR)
    The receiver immediately stops its current operations and is disabled, whatever its current state!
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 12: Start Detection and Data Sampling
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
A low level (space) on URXD is interpreted as a valid start bit
  if it is detected for more than 7 cycles of the sampling clock
  Sampling clock = 16 x baud rate
The receiver samples the URXD at the theoretical midpoint of each bit
  When a valid start bit has been detected
  It is assumed that each bit lasts 16 cycles of the sampling clock (1-bit period): the bit sampling point is eight cycles (0.5-bit period) after the start of the bit
  The first sampling point is therefore 24 cycles (1.5-bit periods) after the falling edge of the start bit was detected
  Each subsequent bit is sampled 16 cycles (1-bit period) after the previous one
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 13: Start Detection and Data Sampling
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 14: Receiver Ready
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
When a complete character is received
  Is transferred to the receive holding register (UART_RHR )
  The RXRDY status bit in UART_SR (Status Register) is set
  The bit RXRDY is automatically cleared when the UART_RHR is read
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 15: Receiver Overrun
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
If UART_RHR has not been read by the software (or the Peripheral Data Controller or DMA Controller) since the last transfer
  and a new character is received
    the OVRE status bit in UART_SR is set
OVRE is cleared when the software writes the control register UART_CR with the bit RSTSTA (Reset Status) at 1
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 16: Transmitter
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The UART transmitter is disabled after device reset
  To enable: TXEN = 1 in the control register UART_CR
    The transmitter waits for a character to be written in the Transmit Holding Register (UART_THR) before actually starting the transmission
  To disable: TXDIS = 1 in the control register UART_CR
    If the transmitter is not operating, it is immediately stopped
    If a character is being processed into the Shift Register and/or a character has been written in the Transmit Holding Register, the characters are completed before the transmitter is stopped
  To reset: RSTTX = 1 in the UART_CR
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 17: Transmitter Control
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
When enabled, the bit TXRDY is set in the UART_SR
The transmission starts when
  The programmer writes in the UART_THR and
  The written character is transferred from UART_THR to the Shift Register
  The TXRDY bit remains high until a second character is written in UART_THR
As soon as the first character is completed
  The last character written in UART_THR is transferred into the shift register and TXRDY rises again
    Showing that the holding register is empty
When both the Shift Register and UART_THR are empty
  All the characters written in UART_THR have been processed
  The TXEMPTY bit rises after the last stop bit has been completed
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 18: Transmitter Control
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 19: UART Registers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
UART Control Register: UART_CR
  RSTRX: Reset Receiver
  RSTTX: Reset Transmitter
  RXEN: Receiver Enable
  RXDIS: Receiver Disable
  TXEN: Transmitter Enable
  TXDIS: Transmitter Disable
  RSTSTA: Reset Status Bits (Resets the status bits PARE, FRAME and OVRE in the UART_SR)

## Slide 20: UART Registers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
UART Mode Register: UART_MR

## Slide 21: UART Registers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
UART Interrupt Enable Register: UART_IER
  RXRDY: Enable RXRDY Interrupt
  TXRDY: Enable TXRDY Interrupt
  ENDRX: Enable End of Receive Transfer Interrupt
  ENDTX: Enable End of Transmit Interrupt
  OVRE: Enable Overrun Error Interrupt
  FRAME: Enable Framing Error Interrupt
  PARE: Enable Parity Error Interrupt
  TXEMPTY: Enable TXEMPTY Interrupt
  TXBUFE: Enable Buffer Empty Interrupt
  RXBUFF: Enable Buffer Full Interrupt
UART Interrupt Disable Register UART Interrupt Mask Register
UART Status Register

## Slide 22: UART Registers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
UART Receiver Holding Register: UART_RHR
  Read-only
  RXCHR: Received Character
    Last received character if RXRDY is set
UART Transmit Holding Register: UART_THR
  Write-only
  TXCHR: Character to be Transmitted
  Next character to be transmitted after the current character if TXRDY is not set

## Slide 23: UART Registers
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
UART Baud Rate Generator Register: UART_BRGR
  CD: Clock Divisor
  0 = Baud Rate Clock is disabled
  1 to 65,535 = MCK / (CD x 16)

## Slide 24
Microprocessors and Assembly Language, Spring 2020, AUT, Tehran, Iran
The End (for now)!